## Slide 1: - 09CE1401 - COMPUTER ORGANIZATION
Prof. Rushi Raval
Marwadi University
Diploma Computer Engineering

## Slide 2: Instruction Codes

## Slide 3: Instruction Codes
Program
  A program is a set of instructions that specify the operations, operands and the sequence by which processing has to occur.

## Slide 4: Instruction Codes
Computer Instruction
  A computer instruction is a binary code that specifies a sequence of micro-operations for the computer.
  The computer reads each instruction from memory and places it in a control register.
  The control then interprets the binary code of the instruction and proceeds to execute it by issuing a sequence of micro-operations.

## Slide 5: Instruction Codes
Instruction Code
  An instruction code is a group of bits that instruct the computer to perform a specific operation.
  Example
ADD 1022

## Slide 6: Instruction Codes
Operation Code (Opcode)
  The operation code of an instruction is a group of bits that define such operations as add, subtract, multiply, shift, and complement.
  The number of bits required for the operation code of an instruction depends on the total number of operations available in the computer.
  The operation code must consist of at least n bits for a given 2n (or less) distinct operations.
ADD 1022

## Slide 7: Stored Program Organization

## Slide 8: Stored Program Organization
Operand
(data)
Instructions
(program)
Memory
4096 x 16
Processor Register (accumulator or AC)
Opcode
Address
0
11
12
15
Instruction Format
Binary Operand
0
15

## Slide 9: Stored Program Organization
The simplest way to organize a computer is to have one processor register(AC) and an instruction code format with two parts.
  The first part specifies the operation (opcode) to be performed and the second specifies an address (operand).
The memory address tells the control where to find an operand in memory.

## Slide 10: Stored Program Organization
This operand is read from memory and used as the data to be operated on together with the data stored in the processor register.
Instructions are stored in one section of memory and data in another.
For a memory unit with 4096 words, we need 12 bits to specify an address since 212 = 4096.

## Slide 11: Stored Program Organization
If we store each instruction code in one 16-bit memory word, we have available four bits for operation code (opcode) to specify one out of 16 possible operations, and 12 bits to specify the address of an operand.
The control reads a 16-bit instruction from the program portion of memory.

## Slide 12: Stored Program Organization
It then executes the operation specified by the operation code.

## Slide 13: Instruction format of Basic Computer

## Slide 14: Instruction format of basic computer
0
11
12
15
Instruction Format
Opcode
Address
I
14
0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1
Add Instruction – ADD 457

## Slide 15: Direct & Indirect Addressing of Memory

## Slide 16: Direct & Indirect Addressing of Memory
ADD
521
0
22
Operand
521
Memory
AC
+
ADD
350
1
35
Operand
1500
Memory
AC
+
1500
350

## Slide 17: Direct & Indirect Addressing of Memory
If the second part of an instruction format specifies the address of an operand, the instruction is said to have a direct address.
In Indirect address, the bits in the second part of the instruction designate an address of a memory word in which the address of the operand is found.

## Slide 18: Direct & Indirect Addressing of Memory
A direct address instruction is placed at address 22 in memory.
The I bit is 0, so the instruction is recognized as a direct address instruction.
The opcode specifies an ADD instruction, and the address part is the binary equivalent of 457.
The control finds the operand in memory at address 457 and adds it to the content of AC.
0
11
12
15
ADD
457
0
14
22

## Slide 19: Direct & Indirect Addressing of Memory
The instruction in address 35 has a mode bit I = 1, recognized as an indirect address instruction.
The address part is the binary equivalent of 350.
The control goes to address 350 to find the address of the operand.
The address of the operand in this case is 350.
The operand found in address 350 is then added to the content of AC.
0
11
12
15
ADD
350
1
14
35

## Slide 20: Computer Instruction

## Slide 21: Computer Instruction
Computer instructions are a set of machine language instructions that a particular processor understands and executes. A computer performs tasks on the basis of the instruction provided.
Computer Instructions contains
  Mode / I bit
  OpCode
  Address

## Slide 22: Computer Instruction
A basic computer has three instruction code formats which are:
  Memory - reference instruction
  Register - reference instruction
  Input - Output instruction

## Slide 23: Computer Instruction
Memory - reference instruction
Here Opcode ranges from 000 to 110
And I (Mode) bit is 0/1 depend on the type of addressing (direct/indirect)
In Memory reference instruction, 12 bits of memory location is specified to address the location of memory
OpCode
Address
I bit

## Slide 24: Computer Instruction
Register - reference instruction
Here Opcode is set to 111 and I (Mode) bit is set to 0
A Register-reference instruction specifies an operation on or a test of the AC (Accumulator) register.
111
Register Operation
0

## Slide 25: Computer Instruction
Input Output instruction
Here Opcode is set to 111 and I (Mode) bit is set to 1
Just like the Register-reference instruction, an Input-Output instruction does not need a reference to memory and is recognized by the operation code 111 with a 1 in the leftmost bit of the instruction. The remaining 12 bits are used to specify the type of the input-output operation or test performed.
111
IO Operation
1

## Slide 26: Computer Instruction
The three operation code bits in positions 12 through 14 should be equal to 111. Otherwise, the instruction is a memory-reference type, and the bit in position 15 is taken as the addressing mode I.
When the three operation code bits are equal to 111, control unit inspects the bit in position 15. If the bit is 0, the instruction is a register-reference type. Otherwise, the instruction is an input-output type having bit 1 at position 15.

## Slide 27: Basic Set of Instructions

## Slide 28: Basic Set of Instructions
Memory Reference Instructions
  Instructions references memory address
  I Bit is 0 / 1 Depending on direct or indirect addressing
  Opcode ranges form 000 to 110
Symbol | Hexadecimal Code |  | Description
AND | 0xxx | 8xxx | And memory word to AC
ADD | 1xxx | 9xxx | Add memory word to AC
LDA | 2xxx | Axxx | Load memory word to AC
STA | 3xxx | Bxxx | Store AC content in memory
BUN | 4xxx | Cxxx | Branch Unconditionally
BSA | 5xxx | Dxxx | Branch and Save Return Address
ISZ | 6xxx | Exxx | Increment and skip if 0

## Slide 29: Basic Set of Instructions
Register Reference Instructions
  Instructions performed on register (Generally AC)
  I Bit is 0, and OpCode is set to 111.
  Bit 0 to 11 represents the operation

## Slide 30: Basic Set of Instructions
Symbol | Hexadecimal Code | Description
CLA | 7800 | Clear AC
CLE | 7400 | Clear E(overflow bit)
CMA | 7200 | Complement AC
CME | 7100 | Complement E
CIR | 7080 | Circulate right AC and E
CIL | 7040 | Circulate left AC and E
INC | 7020 | Increment AC
SPA | 7010 | Skip next instruction if AC > 0
SNA | 7008 | Skip next instruction if AC < 0
SZA | 7004 | Skip next instruction if AC = 0
SZE | 7002 | Skip next instruction if E = 0
HLT | 7001 | Halt computer

## Slide 31: Basic Set of Instructions
IO Reference Instructions
  Instructions performed on Input Output information
  I Bit is 1, and OpCode is set to 111.
  Bit 0 to 11 represents the operation
Symbol | Hexadecimal Code | Description
INP | F800 | Input character to AC
OUT | F400 | Output character from AC
SKI | F200 | Skip on input flag
SKO | F100 | Skip on output flag
ION | F080 | Interrupt On
IOF | F040 | Interrupt Off

## Slide 32: Instruction Set Completeness

## Slide 33: Instruction Set Completeness
A set of instructions is said to be complete if the computer includes a sufficient number of instructions in each of the following categories:
  Arithmetic, logical and shift instructions
  A set of instructions for moving information to and from memory and processor registers.
  Instructions which controls the program together with instructions that check status conditions.
  Input and Output instructions

## Slide 34: Instruction Set Completeness
Arithmetic, logic and shift instructions provide computational capabilities for processing the type of data the user may wish to perform.
A huge amount of binary information is stored in the memory unit, but all computations are done in processor registers. Therefore, one must possess the capability of moving information between these two units.

## Slide 35: Instruction Set Completeness
Program control instructions such as branch instructions are used change the sequence in which the program is executed.
Input and Output instructions act as an interface between the computer and the user. Programs and data must be transferred into memory, and the results of computations must be transferred back to the user.

## Slide 36: Computer Register

## Slide 37: Computer Registers
PC
0
11
IR
0
15
AR
0
11
Program Counter(12)
Holds address of instruction
Address Register(12)
Holds address for memory
Instruction Register(16)
Holds instruction code
Temporary Register(16)
Holds temporary data
Data Register(16)
Holds memory operand
TR
0
15
DR
0
15
INPR
0
7
OUTR
7
Input Register(8)
Holds input character
Output Register(8)
Holds output character
Accumulator(16)
Processor register
0
Memory
4096 words
16 bits per word
AC
0
15

## Slide 38: Common Bus System of Computer

## Slide 39
OUTR
LD
TR
LD
LD
INPR
Memory
4096 x 16
INR
CLR
IR
AC
LD
INR
CLR
DR
LD
INR
CLR
PC
LD
INR
CLR
AR
LD
INR
CLR
Write
Read
Adder & Logic
E
Address
Clock
7
1
2
3
4
5
6
Bus
S2
S1
S0
1

## Slide 40: Control Organization

## Slide 41: Control Organization
Hardwired Control
  The control logic is implemented with gates, flips-flops, decoders and other digital circuits.
  It can be optimized to produce a fast mode of operation.
  It requires changes in the wiring among the various components if the design has to be modified or changed.

## Slide 42: Control Organization
Microprogrammed Control
  The control information is stored in a control memory.
  The control memory is programmed to initiate the required sequence of micro-operations.
  Any required changes or modifications can be done by updating the microprogram in control memory.

## Slide 43: Control Unit of Basic Computer

## Slide 44
15 | 14 | 13 | 12 | 11 - 0
Instruction Register
Control Logic Gates
3 x 8
Decoder
7 6 5 4 3 2 1 0
4 x 16
Decoder
15 14 . . . 2 1 0
I
4-bit sequence counter (SC)
Other inputs
Control O/p
D0
D7
T15
T0
Increment (INR)
Clear (CLR)
Clock
0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1
D1
1
0
0
0

## Slide 45: Control Unit of Basic Computer
An instruction read from memory is placed in the instruction register (IR).
In control unit the IR is divided into three parts: I bit, the operation code (12-14)bit, and bits 0 through 11.
The operation code in bits 12 through 14 are decoded with a 3 x 8 decoder.

## Slide 46: Control Unit of Basic Computer
Bit-15 of the instruction is transferred to a flip-flop designated by the symbol I.
The eight outputs of the decoder are designated by the symbols D0 through D7.
Bits 0 through 11 are applied to the control logic gates.

## Slide 47: Control Unit of Basic Computer
The 4‐bit sequence counter can count in binary from 0 through 15. The outputs of counter are decoded into 16 timing signals T0 through T15.
The sequence counter SC can be incremented or cleared synchronously.

## Slide 48: Control Unit of Basic Computer
Most of the time, the counter is incremented to provide the sequence of timing signals out of 4 X 16 decoder.
Once in awhile, the counter is cleared to 0, causing the next timing signal to be T0.

## Slide 49: Timing and Control Example
As an example, consider the case where SC is incremented to provide timing signals T0, T1, T2, T3 and T4 in sequence. At time T4, SC is cleared to 0 if decoder output D3 is active. This is expressed symbolically by the statement
D3T4: SC ← 0
Initially, the CLR input of SC is active.

## Slide 50: Timing and Control Example
The first positive transition of the clock clears SC to 0, which in turn activates the timing T0 out of the decoder.
T0 is active during one clock cycle.
The positive clock transition labeled T0 in the diagram will trigger only those registers whose control inputs are connected to timing signal T0.

## Slide 51
Clock
CLR SC

## Slide 52: Instruction Cycle

## Slide 53: Instruction Cycle
Program is stored in memory as an sequence of instructions. Each instruction cycle consists of below phases
  Fetch instruction from memory
  Decode instruction
  Read effective address if instruction has indirect address
  Execute instruction.

## Slide 54: Instruction Cycle
These four steps are repeated for each instruction and process ends when it encounter HALT instruction.

## Slide 55: Instruction Cycle
Fetch and Decode
  PC (Program Counter) is loaded with first instruction of program.
  Below is the micro operation for fetch and decode.

## Slide 56: Instruction Cycle
Determine type of instruction
  During time 𝑇3, the control unit determines the type of instruction i.e. Memory reference, Register reference or Input-Output instruction.
  If 𝐷7=1 then instruction must be register reference or input-output else memory reference instruction.

## Slide 57
Start
SC ← 0
AR ← PC
IR ← M[AR], PC ← PC + 1
Decode operation code in IR(12-14)
AR ← IR(0-11), I ← IR(15)
D7
I
I
Execute input-output instruction
SC ← 0
Execute
register-reference instruction
SC ← 0
AR ← M[AR]
Nothing
Execute
memory-reference instruction
SC ← 0
(Register or I/O) = 1
= 0 (Memory-reference)
(I/O) = 1
= 0 (register)
(indirect) = 1
= 0 (direct)

## Slide 58: Input-output

## Slide 59
Keyboard
Transmitter Interface
INPR
AC
OUTR
FGO
FGI
Printer
Receiver Interface
Input-Output terminal
Serial communication interface
Computer registers and flip-flop
=0
=1
=1
=0

## Slide 60: Interrupt Cycle

## Slide 61
R
Fetch & Decode instruction
Store return address in location 0
M[0] ← PC
Execute instruction
IEN
FGI
FGO
R ← 1
Branch to location 1
PC ← 1
IEN ← 0
R ← 0
= 0
= 1
Interrupt cycle
Instruction cycle
= 1
= 0
= 1
= 0
= 1
= 0

## Slide 62: Interrupt Cycle
The interrupt cycle is a hardware implementation of a branch and save return address operation.
An interrupt flip-flop R is included in the computer.
When R = 0, the computer goes through an instruction cycle.
During the execute phase of the instruction cycle IEN is checked by the control.

## Slide 63: Interrupt Cycle
If it is 0, it indicates that the programmer does not want to use the interrupt, so control continues with the next instruction cycle.
If IEN is 1, control checks the flag bits.
If both flags are 0, it indicates that neither the input nor the output registers are ready for transfer of information.

## Slide 64: Interrupt Cycle
In this case, control continues with the next instruction cycle. If either flag is set to 1 while IEN = 1, flip-flop R is set to 1.
At the end of the execute phase, control checks the value of R, and if it is equal to 1, it goes to an interrupt cycle instead of an instruction cycle.

## Slide 65: Design of Basic Computer (Flowchart of Basic Computer)

## Slide 66
AR ← PC
IR ← M[AR], PC ← PC + 1
Decode operation code in IR(12-14)
AR ← IR(0-11), I ← IR(15)
D7
I
I
Execute input-output instruction
SC ← 0
Execute
register-reference instruction
SC ← 0
AR ← M[AR]
Nothing
Execute
memory-reference instruction
SC ← 0
(Register or I/O) = 1
= 0 (Memory-reference)
(I/O) = 1
= 0 (register)
(indirect) = 1
= 0 (direct)
Start
SC ← 0, IEN ← 0, R ← 0
R
AR ← 0, TR ← PC
M[AR] ← TR, PC ← 0
PC ← PC + 1, IEN ← 0, R ← 0, SC ← 0
(Instruction cycle) = 0
=1 (Interrupt cycle)