## Slide 1: - 09CE2401 - COMPUTER ORGANIZATION
Prof. Rushi Raval
Marwadi University
Diploma Computer Engineering

## Slide 2: Unit -3 Programming Basic Computer

## Slide 3: Topics Covered
Introduction
Machine Language
Assembly Language
Assembler
Program Loops
Arithmetic and Logic operations
Subroutines

## Slide 4: Machine Language

## Slide 5: Machine Language
Program
Program is list of instructions or statements for directing the computer to perform a required task.

## Slide 6: Categories of Program
Program can be written in many different ways.
  Binary Code
  Octal / Hexadecimal Code
  Symbolic Code
  High Level Programming Language Code

## Slide 7: Categories of Program
Binary Code
This is a sequence of instructions and operands in binary that list the exact representation of instructions as they appear in computer memory.

## Slide 8: Categories of Program
Location | Instruction Code |  |  | 
0 | 0010 | 0000 | 0000 | 0100
1 | 0001 | 0000 | 0000 | 0101
10 | 0011 | 0000 | 0000 | 0110
11 | 0111 | 0000 | 0000 | 0001
100 | 0000 | 0000 | 0101 | 0011
101 | 1111 | 1111 | 1110 | 1001
110 | 0000 | 0000 | 0000 | 0000

## Slide 9: Categories of Program
Octal or hexadecimal code
This is an equivalent translation of the binary code to octal or hexadecimal representation.

## Slide 10: Categories of Program
Location | Instruction
000 | 2004
001 | 1005
002 | 3006
003 | 7001
004 | 0053
005 | FFE9
006 | 0000

## Slide 11: Categories of Program
Symbolic code
The user uses symbols (letters, numerals, or special characters) for the operation part, the address part, and other parts of the instruction code.
Each symbolic instruction can be translated into one binary coded instruction by a special program called an assembler and language is referred to as an assembly language program.

## Slide 12: Categories of Program
Location | Instruction | Comment
000 | LDA 004 | Load first operand into AC
001 | ADD 005 | Add second operand to AC
002 | STA 006 | Store sum in location 006
003 | HLT | Halt computer
004 | 0053 | First operand
005 | FFE9 | Second operand (negative)
006 | 0000 | Store sum here

## Slide 13: Categories of Program
High Level Programming Language
These are special languages developed to reflect the procedures used in the solution of a problem rather than be concerned with the computer hardware behavior. E.g. Fortran, C++, Java, etc.

## Slide 14: Categories of Program
The program is written in a sequence of statements in a form that people prefer to think in when solving a problem.
However, each statement must be translated into a sequence of binary instructions before the program can be executed in a computer.

## Slide 15: Categories of Program
{
  int a, b;
  a = 10;
  b = 20;
  c = a + b;
}

## Slide 16: Assembly Language

## Slide 17: Assembler

## Slide 18: Assembler
An assembler is a program that accepts a symbolic language program and produces its binary machine language equivalent.
The input symbolic program is called the source program and the resulting binary program is called the object program.

## Slide 19: Assembler
The assembler is a program that operates on character strings and produces an equivalent binary interpretation.

## Slide 20: Pseudo Instruction
A pseudo instruction is not a machine instruction but rather an instruction to the assembler giving information about some phase of the translation.

## Slide 21: Pseudo Instruction
Symbol | Information for the Assembler
ORG N | Hexadecimal number N is the memory location for the instruction or operand listed in the following line.
END | Denotes the end of symbolic program.
DEC N | Signed decimal number N to be converted to binary.
HEX N | Hexadecimal number N to be converted to binary

## Slide 22: Machine Instructions - Memory
Symbol | Hexadecimal Code |  | Description
AND | 0xxx | 8xxx | And memory word to AC
ADD | 1xxx | 9xxx | Add memory word to AC
LDA | 2xxx | Axxx | Load memory word to AC
STA | 3xxx | Bxxx | Store AC content in memory
BUN | 4xxx | Cxxx | Branch Unconditionally
BSA | 5xxx | Dxxx | Branch and Save Return Address
ISZ | 6xxx | Exxx | Increment and skip if 0

## Slide 23: Machine Instructions - Register
Symbol | Hexadecimal Code | Description
CLA | 7800 | Clear AC
CLE | 7400 | Clear E(overflow bit)
CMA | 7200 | Complement AC
CME | 7100 | Complement E
CIR | 7080 | Circulate right AC and E
CIL | 7040 | Circulate left AC and E
INC | 7020 | Increment AC
SPA | 7010 | Skip next instruction if AC > 0
SNA | 7008 | Skip next instruction if AC < 0
SZA | 7004 | Skip next instruction if AC = 0
SZE | 7002 | Skip next instruction if E = 0
HLT | 7001 | Halt computer

## Slide 24: Machine Instructions – I / O
Symbol | Hexadecimal Code | Description
INP | F800 | Input character to AC
OUT | F400 | Output character from AC
SKI | F200 | Skip on input flag
SKO | F100 | Skip on output flag
ION | F080 | Interrupt On
IOF | F040 | Interrupt Off

## Slide 25: Example Program
Location |  | Instruction
 |  | ORG 100
100 |  | LDA SUB
101 |  | CMA
102 |  | INC
103 |  | ADD MIN
104 |  | STA DIF
105 |  | HLT
106 | MIN, | DEC 83
107 | SUB, | DEC -23
108 | DIF, | HEX 0
 |  | END
Symbol | Location
MIN | 106
SUB | 107
DIF | 108

## Slide 26: First Pass of an assembler

## Slide 27: First Pass of an assembler
LC ← 0
Scan next line of code
Label
Store address in symbol table together with value of LC
Increment LC
Set LC
ORG
END
Go to second pass
First pass
no
no
no
yes
yes
yes

## Slide 28: Second Pass of an assembler

## Slide 29
LC ← 0
Scan next line of code
Pseudo-instruction
Store binary equivalent of instruction in location given by LC
Increment LC
Set LC
ORG
END
Second pass
Yes
No
No
No
Yes
Yes
Done
Convert operand to binary and store in location given by LC
MRI
No
Valid non-MRI instruction
Get operation code and set bits 2-4
Search address-symbol table for binary equivalent of symbolic address and set bits 5-16
I
Set first bit to 1
Set first bit to 0
Yes
No
Assemble all parts of binary instruction and store in location given by LC
Yes
Error in line of code
No
Yes
DEC or HEX

## Slide 30: Program for Subroutines

## Slide 31: Program for Subroutines
ORG 100
100
LDA X
101
BSA SH4
102
STA X
103
LDA Y
104
BSA SH4
105
STA Y
106
HLT
107
HEX 1234
X,
108
HEX 4321
Y,
109
HEX 0
10A
CIL
10B
CIL
10C
CIL
10D
CIL
10E
AND MSK
10F
BUN SH4 I
110
HEX FFF0
MSK,
END
SH4,

## Slide 32: I/O Programming

## Slide 33: I/O Programming
1
ORG 100
/Origin of program is HEX 100
2
SKI
/Check input flag
3
BUN CIF
/Flag = 0, branch to check again
4
INP
/Flag = 1, input character
5
OUT
/Print character
6
CHR,
STA CHR
/Store character
7
HLT
8
-
/Store character here
9
END
CIF,
Input Program

## Slide 34: I/O Programming
1
ORG 100
/Origin of program is HEX 100
2
LDA CHR
/Load character into AC
3
SKO
/Check output flag
4
BUN COF
/Flag = 0, branch to check again
5
OUT
/Flag = 1, output character
CHR,
6
HLT
7
HEX 0057
/Character is “W”
8
END
COF,
Output Program